## Slide 1: What does this C code do?
int foo(char *s) {
int L = 0;
while (*s++) {
++L;
}
return L;
}

## Slide 2: Pointers, the Spiral Rule, and Structs
How to read C type declarations
C Strings
  ASCII and null-termination
Array Indexing vs. Pointers
  Pointer arithmetic, in particular
Structs
  Non-homogenous arrays
  Padding

## Slide 3: Representing strings
A C-style string is represented by an array of bytes.
  Elements are one-byte ASCII codes for each character.
  A 0 value marks the end of the array.
32 | space |  | 48 | 0 |  | 64 | @ |  | 80 | P |  | 96 | ` |  | 112 | p
33 | ! |  | 49 | 1 |  | 65 | A |  | 81 | Q |  | 97 | a |  | 113 | q
34 | ” |  | 50 | 2 |  | 66 | B |  | 82 | R |  | 98 | b |  | 114 | r
35 | # |  | 51 | 3 |  | 67 | C |  | 83 | S |  | 99 | c |  | 115 | s
36 | $ |  | 52 | 4 |  | 68 | D |  | 84 | T |  | 100 | d |  | 116 | t
37 | % |  | 53 | 5 |  | 69 | E |  | 85 | U |  | 101 | e |  | 117 | u
38 | & |  | 54 | 6 |  | 70 | F |  | 86 | V |  | 102 | f |  | 118 | v
39 | ’ |  | 55 | 7 |  | 71 | G |  | 87 | W |  | 103 | g |  | 119 | w
40 | ( |  | 56 | 8 |  | 72 | H |  | 88 | X |  | 104 | h |  | 120 | x
41 | ) |  | 57 | 9 |  | 73 | I |  | 89 | Y |  | 105 | I |  | 121 | y
42 | * |  | 58 | : |  | 74 | J |  | 90 | Z |  | 106 | j |  | 122 | z
43 | + |  | 59 | ; |  | 75 | K |  | 91 | [ |  | 107 | k |  | 123 | {
44 | , |  | 60 | < |  | 76 | L |  | 92 | \ |  | 108 | l |  | 124 | ¦
45 | - |  | 61 | = |  | 77 | M |  | 93 | ] |  | 109 | m |  | 125 | }
46 | . |  | 62 | > |  | 78 | N |  | 94 | ^ |  | 110 | n |  | 126 | ~
47 | / |  | 63 | ? |  | 79 | O |  | 95 | _ |  | 111 | o |  | 127 | del

## Slide 4: Strings in C are terminated by the null character (0)
For example, “Harry Potter” can be stored as a 13-byte array.
72 | 97 | 114 | 114 | 121 | 32 | 80 | 111 | 116 | 116 | 101 | 114 | 0
H | a | r | r | y |  | P | o | t | t | e | r | \0

## Slide 5: 2-dimensional arrays in C are laid out in memory as one big array
E.g., int A[100][200]is essentially int A[20000]
“row major order” = rows are laid out contiguously
  A[i][j+1] comes right after A[i][j]
  A[i+1][0] comes right after A[i][199]
  &A[i][j] = &A[0][0] + ((i * 200) + j) * sizeof(int)
A[0][0] | A[0][1] | A[0][2] | A[0][3]
A[1][0] | A[1][1] | A[1][2] | A[1][3]
A[2][0] | A[2][1] | A[2][2] | A[2][3]
A[3][0] | A[3][1] | A[3][2] | A[3][3]
&A | A[0][0]
&A+4 | A[0][1]
&A+8 | A[0][2]
&A+12 | A[0][3]
&A+16 | A[1][0]
&A+20 | A[1][1]
&A+24 | A[1][2]
&A+28 | A[1][3]
&A+32 | A[2][0]
&A+36 | A[2][1]
&A+40 | A[2][2]
&A+44 | A[2][3]
&A+48 | A[3][0]
&A+52 | A[3][1]
&A+56 | A[3][2]
&A+60 | A[3][3]

## Slide 6: Array Indexing Implementation of strlen
Which of the following lines of code correctly loads the contents of string[len] into $t0, assume that len is stored in $v0
lb $t0, $v0($a0) b) add $t0, $a0, $v0
lb $t0, 0($t0)
c) Both (a) and (b)
d) Neither (a) nor (b)
int strlen(char *string) {
int len = 0;
while (string[len] != 0) {
len ++;
}
return len;
}

## Slide 7: Convert the C code into MIPS assembly
int strlen(char *string) {
int len = 0;
while (string[len] != 0) {
len ++;
}
return len;
}

## Slide 8: Assembly coding can help you gain a better understanding of pointers
int strlen(char *string) {
int len = 0;
while (string[len] != 0) {
len ++;
}
return len;
}
int strlen(char *string) {
int len = 0;
while (*string != 0) {
string ++;
len ++;
}
return len;
}

## Slide 9: A pointer is an address
Two pointers that point to the same thing hold the same address
Dereferencing a pointer means loading from the pointer’s address
0x00004000 | 'c'
0x00004001 | 'h'
0x00004002 | 'a'
0x00004003 | 'r'
0x00004004 | 0xFF
0x00004005 | 0xFF
0x00004006 | 0xFF
0x00004007 | 0xF9
char *char2 = 0x4001
char *char1 = 0x4001
int *x = 0x4004
*char1
*x
}
lb or lbu
lw

## Slide 10: The type of a pointer tells us what kind of load to do
Use load byte (lb) for char *
Use load half (lh) for short *
Use load word (lw) for int *
Use load single precision floating point (l.s) for float *

## Slide 11: Pointer arithmetic is often used with pointers to arrays
Incrementing a pointer (i.e., ++) makes it point to the next element
The amount added to the pointer depends on the type of pointer
  pointer = pointer + sizeof(pointer’s type)
  1 for char *, 4 for int *, 4 for float *, 8 for double *
0x00004000 | 'c'
0x00004001 | 'h'
0x00004002 | 'a'
0x00004003 | 'r'
0x00004004 | 0xFF
0x00004005 | 0xFF
0x00004006 | 0xFF
0x00004007 | 0xF9
0x00004008 | 0x00
0x00004009 | 0x00
0x0000400A | 0x00
0x0000400B | 0x09
char string[4] = {'c','h','a','r'};
int array[2] = {-7, 9};

## Slide 12: Convert the C code to MIPS assembly to understand what is going on
int strlen(char *string) {
int len = 0;
while (*string != 0) {
string ++;
len ++;
}
return len;
}

## Slide 13: i>clicker
Suppose I modified the C code to an integer array from a string.
int numNotZero(int *array) {
int len = 0;
while (*array != 0) {
array ++;
len ++;
}
return len;
}
Which of the following lines of code would correctly execute the instruction array ++?
add $a0, $a0, 1 b) add $a0, $a0, 2
c) add $a0, $a0, 4 d) The C code’s behavior is undefined

## Slide 14: Clockwise/Spiral Rule
http://c-faq.com/decl/spiral.anderson.html
Parse any C declaration in your head!
Starting with the unknown element, move in a spiral/clockwise direction; when encountering the following elements replace them with the corresponding English statements:
  [X] or [] => Array X size of... or Array undefined size of...
  (type1, type2) => function passing type1 and type2 returning...
  * => pointer(s) to...
Keep doing this in a spiral/clockwise direction until all tokens have been covered.
Always resolve anything in parenthesis first!
char *str[10];

## Slide 15: More Examples (Arrays and Pointers)
    int *x[];
    int (*y)[];

## Slide 16: More Examples (Const and Pointers)
const char *chptr;
char * const chptr;
chptr is …
A character that points to a constant
A pointer to a char
A constant pointer to a char
A pointer to a constant char

## Slide 17: More Examples (Functions and Pointers)
int *z(int);
int (*q)(int);
q is …
A pointer to an integer
A pointer to an integer that is multiplied with a different integer
A function that takes an integer and returns a pointer to an integer
A function that takes a pointer to an integer and returns an integer
A pointer to a function that takes an integer and returns an integer

## Slide 18: Compilers/assemblers insert padding to “naturally align” data in structs
Structs are like arrays, but the elements can be different types.
  Same with objects
Sometimes you can reorganize fields to eliminate padding.
Structs must align to the largest data type
struct {
int a;
char b;
short c[4];
int d;
}

## Slide 19: How big is this structure?
struct{
char c;
char *c_ptr[4];
}
4 bytes
5 bytes
8 bytes
17 bytes
20 bytes

## Slide 20: Summary
Pointers are just addresses!!
  “Pointees” are locations in memory
Pointer arithmetic updates the address held by the pointer
  “string ++” points to the next element in an array
  Pointers are typed so address is incremented by sizeof(pointee)