## Slide 1: ECE408 / CS483/CSE408 Spring 2018 Applied Parallel Programming Lecture 1: Introduction

## Slide 2: Course Goals
Learn to program massively parallel processors and achieve
  High performance
  Functionality and maintainability
  Scalability across future generations
Technical subjects
  Parallel programming basics
  Principles and patterns of parallel algorithms
  Programming API, tools and techniques
  Processor architecture features and constraints
  Killer apps

## Slide 3: People
Instructors:
  Prof. Wen-mei Hwu
  215 CSL, w-hwu@illinois.edu, 244-8270
  use ECE408 to start your e-mail subject line
  Office hours: 1:30-2:30pm Tuesdays; or by appointment
Teaching Assistants:
  Carl Pearson (pearson@illinois.edu), Keven Feng (klfeng2@illinois.edu), Lan, Rui (ruilan2@illinois.edu) Wei Ren (weiren2@illinois.edu)
  Office hours: Check the course website

## Slide 4: Brief Bio of Wen-mei Hwu
Ph.D. from University of California, Berkeley, 1987
Research: Computer Architecture and Parallel Computing
Professor of ECE Illinois since 1987
Chief Scientist Parallel Computing Institute, Co-PI Blue Waters
Director of several research centers, most recently IBM C3SR
Co-Founder, Advisor and Board Member to 8 startups to date
Researcher, teacher, author, technologist, and entrepreneur

## Slide 5: How we will run the course
Previously recorded lecture video for each major topical segment is on-line.
  In Class Schedule page of course wiki
  Your responsibility is to absorb BEFORE corresponding lecture
Lectures by me when I am in town.
View previously recorded lecture videos when I am traveling – One of the TAs will come to class to discuss finer points, answer questions (flipped class).

## Slide 6: Web Resources
Website: https://wiki.illinois.edu/wiki/display/ECE408/
  Use your Illinois NetID and Password to login
  Handouts and lecture slides/recordings
  Textbook chapters, documentation, software resources
  Note: While we’ll make an effort to post announcements on the web, we can’t guarantee it, and won’t make any allowances for people who miss things in class.
Web board discussions in Piazza
  Channel for electronic announcements
  Forum for Q&A - the TAs and Professors read the board, and your classmates often have answers
Compass - grades

## Slide 7: Grading
Exams: 40%
  Exam 1: 20%
  Exam 2: 20%
Labs (Machine Problems): 35%
  Passing Datasets 90%
  Reasonable-looking answers to questions
Project: 25%
  Automatic Demo/Functionality/Coding Style: 50%
  Automatic Performance Ranking with full functionality: 50%
  Detailed Rubric will be posted

## Slide 8: Academic Honesty
You are allowed and encouraged to discuss assignments with other students in the class. Getting verbal advice/help from people who’ve already taken the course is also fine.
Any reference to assignments from previous terms or web postings is unacceptable
Any copying of non-trivial code is unacceptable
  Non-trivial = more than a line or so
  Copying includes reading someone else’s code and then going off to write your own.

## Slide 9: Academic Honesty (cont.)
Giving/receiving help on an exam is unacceptable
Penalties for academic dishonesty:
  Zero on the assignment/exam for the first occasion
  Automatic failure of the course for repeat offenses

## Slide 10: Text/Notes
D. Kirk and W. Hwu, “Programming Massively Parallel Processors – A Hands-on Approach,” Morgan Kaufman Publisher, 3rd edition, 2016, ISBN 978-0123814722
    all chapters used in this course are in Wiki
NVIDIA, NVidia CUDA C Programming Guide, version 7.5 or later (reference book)

## Slide 11: Tentative Schedule (Class Schedule Tab in Wiki)
Week 1:
  Tu: Lecture 1: Introduction
  Th: Lecture 2: CUDA Intro
Week 2:
  Tu: Lecture 3: Data Parallelism Model
  Th: Lecture 4: CUDA Memory Model
  Due: MP-0, installation, test account, MP-1, vector addition
Week 3:
  Tu: Lecture 5: CUDA Memory Model
  Th: Lecture 6: Performance Considerations
  Due: MP-2, simple matrix multiplication

## Slide 12
A major paradigm shift
In the 20th Century, we were able to understand, design, and manufacture what we can measure
  Physical instruments and computing systems allowed us to see farther, capture more, communicate better, understand natural processes, control artificial processes…

## Slide 13
A major paradigm shift
In the 21st Century, we are able to understand, design, and create what we can compute
  Computational models are allowing us to see even farther, going back and forth in time, learn better, test hypothesis that cannot be verified any other way, create safe artificial processes…

## Slide 14: Examples of Paradigm Shift
20th Century
Small mask patterns
Electronic microscope and Crystallography with computational image processing
Anatomic imaging with computational image processing
Teleconference
GPS
21st Century
Optical proximity correction
Computational microscope with initial conditions from Crystallography
Metabolic imaging sees disease before visible anatomic change
Tele-emersion
Self-driving cars

## Slide 15: Post-Dennard technology pivot – Parallelism and heterogeneity

## Slide 16: Dennard Scaling of MOS Devices
  In this ideal scaling, as L → α*L
  VDD → α*VDD, C → α*C, i → α*i
  Delay = CVDD/I scales by α, so f → 1/α
  Power for each transistor is CV2*f and scales by α2
    keeping total power constant for same chip area
JSSC Oct 1974, page 256

## Slide 17: Frequency Scaled Too Fast 1993-2003

## Slide 18: Total Processor Power Increased (super-scaling of frequency and chip size)

## Slide 19
Post-Dennard Pivoting
Multiple cores with more moderate clock frequencies
Heavy use of vector execution
Employ both latency-oriented and throughput-oriented cores
3D packaging for more memory bandwidth

## Slide 20: Blue Waters Computing System Operational at Illinois since 3/2013
Sonexion: 26 PBs
>1 TB/sec
100 GB/sec
10/40/100 Gb
Ethernet Switch
Spectra Logic: 300 PBs
120+ Gb/sec
WAN
IB Switch
12.5 PF
1.6 PB DRAM
$250M
49,504 CPUs -- 4,224 GPUs
Notes: Note just compute – main memory (1.6PB); Disk (26PB); near line (300PB)

## Slide 21: Cray XK7 Compute Node
Y
X
Z
HT3
HT3
PCIe Gen2
XK7 Compute Node Characteristics
AMD Series 6200 (Interlagos)
NVIDIA Kepler
Host Memory 32GB 1600 MT/s DDR3
NVIDIA Tesla X2090 Memory 6GB GDDR5 capacity
Gemini High Speed Interconnect
Keplers in final installation

## Slide 22: Qualcomm SoC for Mobile

## Slide 23: CPUs: Latency Oriented Design
High clock frequency
Large caches
  Convert long latency memory accesses to short latency cache accesses
Sophisticated control
  Branch prediction for reduced branch latency
  Data forwarding for reduced data latency
Powerful ALU
  Reduced operation latency
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU

## Slide 24: GPUs: Throughput Oriented Design
Moderate clock frequency
Small caches
  To boost memory throughput
Simple control
  No branch prediction
  No data forwarding
Energy efficient ALUs
  Many, long latency but heavily pipelined for high throughput
Require massive number of threads to tolerate latencies
DRAM
GPU

## Slide 25: Applications Benefit from Both CPU and GPU
CPUs for sequential parts where latency matters
  CPUs can be 10+X faster than GPUs for sequential code
GPUs for parallel parts where throughput wins
  GPUs can be 10+X faster than CPUs for parallel code

## Slide 26: Winning Strategies Use Both CPU and GPU
CPUs for sequential parts where latency hurts
  CPUs can be 10+X faster than GPUs for sequential code
GPUs for parallel parts where throughput wins
  GPUs can be 10+X faster than CPUs for parallel code

## Slide 27: Heterogeneous Parallel Computing Applications
Financial Analysis
Scientific Simulation
Engineering Simulation
Data Intensive Analytics
Medical Imaging
Digital Audio Processing
Computer Vision
Digital Video Processing
Machine Learning
Electronic Design Automation
Statistical Modeling
Ray Tracing Rendering
Interactive Physics
Numerical Methods
Biomedical Informatics

## Slide 28: Parallel Programming Work Flow
Identify compute intensive parts of an application
Adopt/create scalable algorithms
Optimize data arrangements to maximize locality
Performance Tuning
Pay attention to code portability, scalability, and maintainability

## Slide 29: Parallelism Scalability

## Slide 30: Algorithm Complexity and Data Scalability

## Slide 31: A Real Example of Data Scalability Particle-Mesh Algorithms

## Slide 32
Massive Parallelism - Regularity

## Slide 33: Load Balance
The total amount of time to complete a parallel job is limited by the thread that takes the longest to finish
good
bad!

## Slide 34: Global Memory Bandwidth
Ideal
Reality

## Slide 35: Conflicting Data Accesses Cause Serialization and Delays
Massively parallel execution cannot afford serialization
Contentions in accessing critical data causes serialization

## Slide 36: What is the stake?
Scalable and portable software lasts through many hardware generations
Scalable algorithms and libraries can be the best legacy we can leave behind from this era

## Slide 37: Any More Questions?